## Slide 1: Dust off your Raspberry Pi
Put your Pi to use and learn embedded development
Raspberry Pi is a trademark of the Raspberry Pi Foundation

## Slide 2: About me
Douglas Gore
Embedded software engineer (6 years)
Work at Nagra Media UK
Primarily work on Set Top Boxes and PVRs
Love to experiment with technology and ideas in my spare time
E.g. JavaScript MOD player, GameBoy emulator, etc
Find me on Twitter @DougGore

## Slide 3: What We will Cover
Introduction to the Pi
The hardware and APIs
Setup
A few interesting programs
High level coding with Qt5 and QtQuick
Low level interfacing
Q&A

## Slide 4: Do you do Pi?
Hands up if you own a Raspberry Pi?
Hands down if you have only run XMBC?
Hands down if you haven’t touched it in a month?
Hands up if you have created or ported software on the Pi?
Notes: Get audience to put their hands up

## Slide 5: Introducing the Pi
Broadcom BCM2835 SoC
Hardware accelerated 3D graphics
Hardware video and audio decoding
H.264 video encoding
256MB RAM split between CPU and GPU
Forget that, it’s now 512MB
Same chip as Roku 2
Programmable pins for custom hardware
And most importantly…
Notes: Roku 2 plays Angry Birds

## Slide 6: NOW Built in WaLes

## Slide 7: The Last Computer Made in Wales?

## Slide 8: …Not Quite

## Slide 9: The Zebra
Zeer Eenvoudige Binaire Reken Automaat

## Slide 10: BBC Model B & electron

## Slide 11: ZX Spectrum

## Slide 12: Torch Computers

## Slide 13: Apple iMAC

## Slide 14: Production in the 80s

## Slide 15: Production now

## Slide 16: The PCB

## Slide 17: What is an SoC?
Slow CPU core, STBs just reaching 1GHz, mobile now approaching 2GHz, many cores
Lots of specialised co-processors for multimedia, DSP, graphics, security
DACs, ADCs, signal generation, front ends often integrated
Push as much processing onto co-processors as possible
Aim is generally to offer something that is just “good enough” for the job to keep costs low

## Slide 18: Package On Package (POP)

## Slide 19: Hardware acceleration
OpenGL ES 2.0 – 3D graphics
  Gaming, slick UI effects, shaders
OpenVG – 2D graphics
  Vector graphics, UI compositing
OpenMAX – Hardware audio and video decoding and encoding
  The official method and only sane way to doing AV decoding

## Slide 20: Where those Apis Sit
Notes: All of this is Open Source

## Slide 21: Codec support
Video
  H.264 – Blu-Ray, web video (YouTube), HDTV, IPTV
  MPEG2 (£2.40) – DVD, SDTV
  VC-1 (£1.20) – Windows Media, Blu-Ray
Audio
  HE-AAC – HDTV, IPTV, web video, DAB+, Internet radio
  AAC – iTunes
  MP3 – Music
  MP2 – DAB, SDTV, DVD
  Dolby + DTS (passthrough)

## Slide 22: Useful APIs and Systems
DirectFB
  Direct access to the framebuffer for drawing, bliting
Simple DirectMedia Layer (SDL)
  Multi-platform API for multimedia, like DirectX
GStreamer
  Pipeline based media architecture, like DirectShow
LiRC
  Standard system for handling IR remotes

## Slide 23: Setup

## Slide 24: Flashing an SD card
Two partitions, a FAT32 partition for the bootloader and a ext4 partition for the OS
Windows users should use a program called Win32DiskImager
Linux geeks, you can use dd and figure it out yourself ;-)
If present on image, use raspi-config to make rest of SD card accessible and configure some basic parameters

## Slide 25: Getting prebuilt software
Start by installing packages that interest you, it’s just normal Linux
Command line tool, apt-get manages common software packages on Debian variants
Syntax “apt-get install <package>”
Some things will work better than others

## Slide 26: Interesting programs
Penguins Puzzle
TinyBASIC
PyGame (Squirrel Eat Squirrel)
RetroArch
Quake 3
Scratch

## Slide 27: Omxplayer
A simple command line media player which uses the hardware acceleration capabilities
Best way to “just play something”
May need to be explicit about outputs used
GStreamer is more advanced but is harder to use

## Slide 28: High level Coding with Qt5
To the code…

## Slide 29: QT5
Cross-platform development environment
Program in a variety of languages
Qt Quick high level UI builder + JavaScript = quick, fast and easy application development
Ideal for designers and web developers
Largely self-contained ecosystem
Runs on a wide variety of hardware and takes advantage of hardware acceleration

## Slide 30: Getting Started
Was in Debian Wheezy, disappeared when Raspbian appeared
You can roll your own but you have to compile it first (sorry)
Handy script called bakeqtpi has been developed
Works on Linux and OSX
Can develop on your PC then deploy to Raspberry Pi (Windows, Linux, Mac)
Easier to get started with Qt Creator IDE

## Slide 31: How does QtQuick work?
Easiest way is to write one or more .qml files and execute them using qmlscene
Eventually you can build a binary and complement with native code
QML = Qt Markup Language
Syntax consists of describing objects and their properties
JavaScript can be inline or external files

## Slide 32: Hello, world
import QtQuick 2.0
Rectangle
{
id: main
width: 1280
height: 720
color: "white"
Text {
id: hello
text: "Hello, world"
font.pointSize: 48
color: "black"
}
}

## Slide 33: Qt5 demo

## Slide 34: Low level Hardware Interfacing

## Slide 35: Low level I/O
Photo used under Creative Commons from EJP Photo
When people tell you programming is just 1s and 0s…
…they’re right you just haven’t entered The Matrix yet

## Slide 36: What’s on the Pi
2 x 13 pinout (some changes on Rev 2)
3.3V and 5V power pins plus ground
8 x GPIO pins
I2C
SPI
UART
PWM

## Slide 37: GPIO programming
GPIO = General Purpose Input Output
The signals on these pins have no specific pre-defined purpose, you are free to control them as you wish
Simplest and most flexible construct
Most basic use is enable/disable
Time and or multiple pins can be used for more complex functionality
Pure software IO is called “bit banging”
IR remote control/receiver

## Slide 38: SPI
Serial Peripheral Interface Bus
Hardware support
4 pins useds
  Serial clock
  Output
  Input
  Chip select
Many useful applications

## Slide 39: Spi applications

## Slide 40: I2C
Inter-Integrated Circuit (or 2 wire)
Just clock and data pins
Very common and widely used
Very easy to program just write device addresses, sub-address (optional) and data

## Slide 41: I2C Applications

## Slide 42: Raspberry Pi Pinout
Colour legend
+5 V
+3.3 V
Ground, 0V
UART
GPIO
SPI
I²C
Make sure you know where pin 1 is!

## Slide 43: Clocks
1 = high, 0 = low
FALLING EDGE

## Slide 44: Two ways to code C/C++
On the target platform directly with normal GNU toolchain make, gcc, etc
Cross compiling from your host (PC) to the target (Pi)
Cross compiling toolchain run on the host but the binaries run on the target
More involved but will be far quicker especially for large complex projects

## Slide 45: Summary
Hardware and API available
Setting up your Pi
Talked about some apps
Introduced Qt5
Covered low level programming

## Slide 46: That’s all folks
Follow me on Twitter @DougGore
Any questions?